## Slide 1: Mem_43_MRAM: two ways to write MRAM
One configuration switch: MemUseAXIInterfaceEnabled (MemAutosarExt, default OFF). It selects how Write and Erase reach the MRAM; Read is the same in both cases.
OFF (default): IPS path
CPU
MRAMC
write registers
MRAM
1. The driver reserves one of the controller's 2 write slots, so no other processor can use it.
2. It copies the data (up to 256 bytes = 8 pages) into the slot and marks which bytes are valid.
3. It tells the controller "write now". The controller writes the data into the memory.
4. The driver waits until the controller answers "done" or "error" for this write.
ON: AXI path
CPU
Write buffer
(32 bytes)
MRAM
1. The processor writes the data straight to the MRAM address, 4 bytes at a time, without waiting.
2. Pieces smaller than 4 bytes: the driver reads the 4 bytes around them, changes them and writes them back.
Notes: IPS = register (peripheral) bus of the MRAMC. AXI = system bus, direct memory-mapped stores. Same Mem_43_MRAM API in both cases.

## Slide 2: Which one should I use?
Question | Switch OFF (default) | Switch ON
Who does the writing? | The memory controller. The processor hands it the data (up to 256 bytes at a time), then waits until the controller says the data is in the memory. | The processor. It writes the data straight to the memory address, 4 bytes at a time, and continues with other work sooner; the controller finishes the writing in the background.
When do I find out that a write failed? | Immediately: after each write the controller reports "done" or "error", so the driver knows exactly which write failed. | Only at the end: the driver checks the error registers after the whole write, so it knows that something failed, but not exactly which part.
Several processors writing at the same time? | Safe: a processor must first reserve a write slot of the controller; the others wait until it is free again. | Not safe by itself: nothing makes the processors wait for each other, so your software must make them take turns.
Small or odd-sized data (e.g. 1 byte)? | Easy: the controller changes only the bytes you write inside the page. | More work: the driver reads the 4 bytes around them, changes them and writes them back, so it is slower.
Choose OFF
the safe choice; use it if you are not sure
Choose ON
only one processor writes, and you want it free for other work sooner
OFF = IPS path, ON = AXI path. Which one is faster overall must be measured on the target.
Notes: Performance is a qualitative statement from the implementation; it has not been benchmarked yet.

## Slide 3: Examples
Write 1 byte (e.g. a status flag)
Switch OFF: One command; the controller merges the byte into its page. Memory written once.
Switch ON: Empties the buffers, reads 4 bytes, writes them back, empties the buffers again. Memory written once, but more steps.
OFF is simpler and likely faster
Write 256 bytes, 4-byte aligned (e.g. a data block)
Switch OFF: One command of 8 pages; the processor waits for the confirmation. Memory: 2 write operations.
Switch ON: 64 direct writes of 4 bytes; the processor moves on sooner. Memory: 8 write operations.
ON frees the processor sooner; total time must be measured
Two processors write MRAM at the same time
Switch OFF: Safe: the controller lets one write in at a time.
Switch ON: Your software must make them take turns.
OFF, unless you already coordinate the writers
Same on both paths: partition locks, cache handling and error reporting. Switch ON: keep the source data outside MRAM. Every write wears the MRAM: write whole 32-byte pages when you can.

## Slide 4: Built-in self-tests of the MRAM (UTest)
Next to your data, the MRAM stores a few extra check bits. With them it can repair small errors when it reads, and raise an alarm for errors it cannot repair.
UTest checks that these protection circuits still work; your data is not changed. Switch: MemHwUTestService (default OFF). Typical use: at start-up or periodically, as your safety concept requires.
Test | What it does | Result
Array integrity check | Reads a whole memory area and combines every word into one short number, a signature. If even one bit in the area is different, the signature is different. | Compare it with the signature you expect (e.g. calculated when the area was programmed). Equal = the area reads back correctly.
ECC logic check | The repair circuit uses the check bits to fix up to 3 wrong bits per read. The test feeds it data with wrong bits on purpose. | Shows whether it repaired 1, 2 or 3 bits, or reported 4.
EDC-after-ECC logic check | A second checker verifies the data again after the repair, to catch a repair that went wrong. The test gives it bad data on purpose. | Shows whether the second checker raised the alarm.
Address-encode logic check | The address is mixed into the check bits, so data read from the wrong place does not match. The test changes address bits on purpose. | Shows whether the wrong address was detected.
Reference recovery and refresh | The MRAM decides 0 or 1 by comparing each bit with internal reference cells. This operation refreshes those cells. | Done or failed.
While a test runs, the MRAM is in test mode: nothing else may use it.